## Slide 1: Motivations to adopt a new approach
Main limitations of the old model (Pizzocri et al. 2023)
Linearization of the diffusion coefficient -> difficulty in capturing exponential behaviour far from the linearization temperature.
Train on a single set of parameters -> no possibility to generalized
Offline phase performed in OpenFOAM -> code sharing requires tool knowledge.
Improvements in the new approach:
Use of a well-established method from the literature instead of linearization for the diffusion coefficient.
Incorporation of multiple parameter sets for better generalization.
Perform offline phase in FreeFEM++ and Python.

## Slide 2: Schematic representation

## Slide 3: Governing equations
Where:
From Pizzocri et al. 2023 the temperature field develops much more rapidly than the concentration field -> decouple the two PDEs and solve the steady state:
solved 1D

## Slide 4: Full order model in FreeFEM++ and Python
Finite element modelling in FreeFEM++
Mesh sensitivity.
Comparison with the OpenFOAM solution:
Error at steady state = 0.08%
Max error = 0.017%

## Slide 5: Reduced order model
Once the dimensional set of spatial reduced basis functions the reduced space is constructed. The full model solution is approximated by:
Being the test functions:
Stiffness matrix
Mass matrix
Source vector

## Slide 6: Reduced order model: training set
The training set of parameters is a sufficiently rich subset of the parameter space obtained by drawing random samples from a uniform distribution
Values determined based on the SUPERFACT-1 (Luzzi et al., 2021; Luzzi et al., 2023) and SPHERE (Lainet et al., 2024) JOYO (Maeda et al., 2009) irradiation experiments.

## Slide 7: DEIM: construction of affine decomposition
computed during the online phase
Discrete Empirical Interpolation Method (DEIM) consists of rewriting as a linear combination:
The stiffness matrix is rewritten in this way:
Notes: Con il DEIM decomponiamo affinamente la stiffness cosi da avere un problema lineare.

## Slide 8: POD-greedy
The greedy methods incrementally expand the approximation by incorporating new basis functions corresponding to states not adequately represented by the current model approximation.

## Slide 9: Online stage in SCIANTIX 2.1
Backward Euler scheme:
Sciantix received as input a single file containing these matrices.

## Slide 10: Online stage in SCIANTIX 2.1: comparison with FOM
Check done with worst reconstructed parameters case:
Maximum error = %
Maximum error = %
Check done with reference case:
Maximum error = %
Maximum error = %

## Slide 11: Computational times
POD-greedy = 27 minutes x -iterations
= 27 minutes x 8 = 3.6 hours
Offline phase:
FreeFEM: 3 minutes
Full order: 7 minutes
POD: 20 minutes
= 3.6 ore
Online phase in sciantix: 5 seconds
Speed-up: 2592

## Slide 12: Diffusion coefficients

## Slide 13: Next steps
Define the dedicated coupling interface between SCIANTIX and TRANSURANUS to account for columnar grains.
Apply the algorithm to integral irradiation cases:
  SUPERFACT-1
  SPHERE

## Slide 14
Thank you for your kind attention

## Slide 15: Literature
Forsberg, K., Massih, A.R., 1985. Fission gas release under time-varying conditions. Journal of Nuclear Materials 127, 141–145. doi:10.1016/0022-3115(85)90348-4.
Olander, D.R., 1976. Fundamental Aspects of Nuclear Reactor Fuel Elements, Technical Information Center – Energy Research and Development Administration, University of California, Berkeley, CA, USA.
Pastore, G., Swiler, L.P., ... Williamson, R.L., 2015. Uncertainty and sensitivity analysis of fission gas behavior in engineering-scale fuel modeling. Journal of Nuclear Materials 456, 398–408. doi:10.1016/j.jnucmat.2014.09.077.
Pastore, G., Pizzocri, D., Luzzi, L., 2018. An effective numerical algorithm for intra-granular fission gas release during non-equilibrium trapping and resolution. Journal of Nuclear Materials 509, 687–699. doi:10.1016/j.jnucmat.2018.07.030.
Pizzocri, D., Rabiti, C., Luzzi, L., Barani, T., Van Uffelen, P., & Pastore, G. 2016. PolyPole-1: An accurate numerical algorithm for intra-granular fission gas release. Journal of Nuclear Materials, 478, 333–342. https://doi.org/10.1016/j.jnucmat.2016.06.028.
Pizzocri, D., Di Gennaro, M., Barani, T., Silva, F. A. B., Zullo, G., Lorenzi, S., & Cammi, A. 2023. A reduced order model for fission gas diffusion in columnar grains. Nuclear Engineering and Technology, 55(11), 3983–3995. https://doi.org/10.1016/j.net.2023.07.013
Sirovich, L., 1987. Turbulence and the dynamics of coherent structures. I. Coherent structures. Quarterly of Applied Mathematics 45, 561–571. doi:10.1090/qam/910462.

## Slide 16
Backup slides

## Slide 17: Proper Orthogonal Decomposition procedure
Proposed by Sirovich 1987 and nowadays represents the state-of-the-art of ROM methods for fluid dynamics applications. Let be the physical domain and let be a set of snapshots related to a certain FOM dependent on the parameter , where:
These functions usually belong to a subspace of the Hilbert Space .
The POD space is constructed solving the following minimization problem:
This minimization can be obtained solving the eigenvalue problem:
Where K is the correlation matrix of snapshots:
The POD modes can be obtained with:

## Slide 18: SUPERFACT
Parameter | Values
Fission rate | 
Cylinder length | 
Cylinder radius | 
Parameter | Values
Fission rate | 
Cylinder length | 
Cylinder radius |